## Slide 1
Status of the JWST Science Instrument Payload
Matt Greenhouse
JWST Project Office
NASA Goddard Space Flight Center
4 July 2016
@NASAWebbTelescp
#JWST

## Slide 2: The Integrated Science Instrument Module (ISIM) is the science instrument payload of the JWST
The ISIM system consists of:
  Five sensors (4 science)
    MIRI, NIRISS, FGS, NIRCam, NIRSpec
  Nine instrument support systems:
    Optical metering structure system
    Electrical Harness System
    Harness Radiator System
    ISIM electronics compartment
    ISIM Remote Services Unit
    Cryogenic Thermal Control System
    Command and Data Handling System
    Flight Software System
    Operations Scripts System
ISIM is one of three elements that together make up the JWST space vehicle
  Approximately 1.4 metric tons, ~20% of JWST by mass
  Element-level I&T completed, ISIM was delivered to OTIS integration during March

## Slide 3: Three ISIM assemblies reside on the cryogenic side of the space vehicle
Four science sensors:
  NIRCam, NIRSpec, NIRISS, MIRI
Fine guidance sensor (FGS)
  Supports telescope pointing to ~ 10-6 deg
Optical metering structure
  Sensor launch loads
  Sensor optical alignment over ~250 deg DT
Harness Radiator (HR)
  Passive cooling for ~2,700 electrical wires
Electronics Compartment (IEC)
  Houses 11 electronics boxes
  Manages 220 W power on cryo side of space vehicle
3

## Slide 4: Flight ISIM test configuration
MIRI
ISIM Electronics Compartment (IEC)
Harness Radiator (HR)
NIRCam
FGS/NIRISS
NIRSpec
4

## Slide 5: ISIM integration with OTE is on schedule for OTIS testing
Key 2016 integration milestones:
ISIM Prime module integration w/ OTE: May
MIRI FPE integration with IEC: Jun
  FPE reworked after CV-3
IEC integration w/ OTE: Aug
Harness Radiator integration w/ OTE: Sep

## Slide 6
NIRCam Flight Model
The NIRCam will image the earliest epoch of galaxy formation

## Slide 7: NIRCam will provide the deepest near-infrared images ever and will identify primeval galaxy targets for the NIRSpec
Developed by the University of Arizona with Lockheed Martin
  Operating wavelength: 0.6 – 5.0 microns
  Field of view: 2.2 x 4.4 arc minutes
  Angular resolution (1 pixel): 32 mas < 2.3 microns, 65 mas > 2.4 microns
  Imagery: R= 4, 10, 100 filters
  Spectroscopy: grisim (slit-less) R~2000 2.4 – 5 microns
  Coronagraph

## Slide 8
FM2 test Jan 2013
NIRSpec can obtain spectra of 100 compact galaxies simultaneously

## Slide 9: Aperture control: 250,000 programmable micro-shutters
Human Hair 90 um Dia.
203 x 463 mas shutter pixel clear aperture, 267 x 528 mas pitch, 4 x 171 x 365 array
Flight MSA

## Slide 10: The NIRSpec will acquire near-infrared spectra of up to 100 objects in a single exposure
Developed by the European Space Technology Center (ESTEC) with Astrium and Goddard Space Flight Center
  Operating wavelength: 0.6 – 5.0 microns
  Spectral resolution: 100, 1000, 3000
  Field of view: 3.4 x 3.4 arc minutes
    Aperture control:
      Programmable micro-shutters, 250,000 pixels
        203 x 463 mas clear aperture (267 x 528 mas pitch)
      Fixed long slits & transit spectroscopy aperture
        200, 400, 1600 mas slit width
      Image slicer (IFU) 3x3 arc sec FOV (100 mas slice width)
  All aperture control modes available with any spectral resolution mode

## Slide 11
MIRI flight model
x
MIRI will provide the first high resolution imagery of the mid-infrared universe

## Slide 12: The MIRI will characterize circumstellar debris disks, extra-solar planets, and the evolutionary state of high redshift galaxies
Developed by a consortium of 10 European countries and NASA/JPL
  Operating wavelength: 5 – 28.5 microns
  Broad-band imagery: 1.9 x 1.4 arc minutes FOV, 110 mas/pixel, 9 filters (R~5)
  Spectroscopy:
    R~100 long slit spectroscopy 5 x 0.2 arc sec
    R~3000 IFU spectroscopy (4 image slicers fed by dichroic beam splitters)
      Slice width: 19, 19, 24, and 27 mas
  Coronagraphic imagery: Three 4QPMs and 1 Lyot occulting mask, 110 mas/pixel
IFU Fields of View

## Slide 13: The MIRI cryo-cooler is complete and delivered to spacecraft I&T
Pre-Ship review completed during May
Flight spare cooler in final verification testing at JPL

## Slide 14: FGS can sense pointing to 1 millionth degree precision NIRISS enables moderate contrast imagery at an inner working angle of 0.5l/D
Flight FGS

## Slide 15: The FGS-Guider and NIRISS provide telescope pointing control imagery & slitless spectroscopy for Ly-a galaxy surveys and extra-solar planet transits
Developed by the Canadian Space Agency with ComDev
FGS: 4 mas noise equivalent angle (0.6 – 5 microns)
  ~95% probability of guide star acquisition over whole sky
  7 mas LOS pointing stability
NIRISS:
  Wide-field slit-less spectroscopic imagery (grism)
    R ~ 150, 0.8 – 2.25 microns optimized for Ly alpha galaxy surveys
  Single object spectroscopic imagery (grism): 3 orders cross-dispersed
    R ~ 700, 0.7 – 2.5 microns optimized for exoplanet transit spectroscopy
  Aperture mask interferometric imaging (7 aperture NRM, 21 unique baselines) 3.8, 4.3, and 4.8 microns (IWA ~ 0.5l/D)
  68 mas/pixel all modes
Simulated NIRISS aperture mask near-infrared image of a 1-2 MJup planet at ~1 AU of a M0V star 10 pc from the Sun.

## Slide 16: JWST will achieve unprecedented infrared sensitivity
However, 30 m ground-based facilities can challenge JWST performance for R > 1000 spectroscopy at wavelengths < 1.7 microns
Mauna Kea
JWST

## Slide 17: Observer take-aways
The ISIM contains a Fine Guidance Sensor that enables the observatory to achieve 7 mas pointing stability
The ISIM includes 4 science sensors that enable:
  Nyquist sampled imagery in broad-band filters
  Coronagraphic imagery with contrast ~104 - 105 over the whole JWST wavelength range
  Slit-less, long slit, and multi-object spectroscopy with R ~ 102 - 103
  IFU spectroscopy over the whole JWST wavelength range
  Interferometric imagery over 4-5 microns with resolution 0.5l/D
All ISIM sensors have sub-array detector readout capability to enable observation of bright targets
All ISIM sensors are designed for simultaneous and continuous operation

## Slide 18
Instrument module integration with OTE
Click Video

## Slide 19: In Sum …
ISIM is on track to support the OTIS end-to-end optical test at JSC during April 2017
Integration of the ISIM system to the OTE is proceeding without issue
Last element-level ISIM test was completed during February 2016 in the GSFC SES chamber
Observatory end-to-end optical test
begins during April 2017 in JSC Chamber-A
Launch 2018 from Kourou Launch Center (French Guiana)