## Slide 1
Niriss overvieW
Chris Willott, René Doyon, and the FGS/NIRISS Team
JWST @ ROE
4 July 2016

## Slide 2: Outline
Instrument overview
Observing modes
NIRISS GTO program overview

## Slide 3: FGS/NIRISS overview
Two instruments in one box
FGS (Fine Guidance Sensor)
  Provides fine guiding to the observatory
  0.6-5 μm IR camera.
  No filters, single optical train with two redundant detectors each with a FOV of 2.3’x2.3’
    Noise equivalent angle (one axis): 4 milliarcsec
    95% sky coverage down to JAB=18.9
NIRISS (Near-Infrared Imager and Slitless Spectrograph)
  0.6-5 μm IR camera similar to NIRCam LW
  Four observing modes
  Main science drivers
    Galaxy evolution
    Exoplanet spectroscopy
    High-contrast imaging

## Slide 4: NIRISS overview 1
1 http://www.stsci.edu/jwst/instruments/niriss/docarchive/NIRISS-pocket-guide.pdf

## Slide 5: Dual wheel optical elements

## Slide 6: Outline
Instrument overview
Observing modes
NIRISS GTO program overview

## Slide 7: Observing modes summary
Single-Object Slitless Spectroscopy (SOSS)
  Optimized for relatively bright stars (e.g. exoplanet transiting systems).
  Wavelength range: 0.6 – 2.8 μm
  Spectral resolution: 500-1500
  Brightness limit: J~7
Aperture Masking Interferometry (AMI, high-contrast imaging)
  Wavelength range: 3.8 – 4.8 μm.
  Three medium-band (5-8%) filters.
  Contrast: 10-4 between 70 and 500 mas on 5th magnitude star at 4.8 μm.
Wide-Field Slitless Spectroscopy (WFSS)
  Main application for high-z galaxies
  Wavelength range: 0.8 – 2.2 μm
  Spectral resolution: 150
  Line flux sensitivity requirement (10σ 104s): 5.4 x10-18 ergs/cm2 at 1.4 μm with F140M filter.
Broad-band imaging (BBI)
  7 NIRCam filters: F090W, F115W, F150W, F200W, F277W, F356W, F444W
  Mode used in support of WFSS observations.
  Can be used as extra field in parallel with NIRCam imaging.
  Instrument could be used without filters to be operated as a guider.
Provide unique science modes plus backup of NIRCam and NIRSpec modes

## Slide 8: Single Object Slitless Spectroscopy

## Slide 9: Single Object Slitless Spectroscopy
Specifically optimized for transit spectroscopy
  Grism with built-in defocussing weak lens to increase dynamic range and minimize systematic ‘’red noise’’ due to undersampling and flatfield errors
  Optical implementation to the successful « scanning mode » used on HST
Broad simultaneous wavelength range: 0.6-2.8 um
  Cross-dispersed (orders 1 and 2), no blocking filter.
Spectral resolution: ~1000 (700 @ 1.2) um in first order
  500-1600 across wavelength range

## Slide 10: SOSS Hardware implementation
Monochromatic PSF measured in the lab
λ
FWHM
CV3 monochromatic PSF
Trace Width (defocus)

## Slide 11: Aperture Masking Interferomery (AMI)

## Slide 12
Probe separations of ~40 to 400 mas
At contrast of up to 9 mag
Filters: F380M, F430M, F480M, (and F277W)
7-aperture mask, in pupil wheel
Image recorded at detector: interferogram
Its Fourier transform amplitude (and phase)
reveals presence of companion
Ground-based L’ & M’ limits
Aperture Masking Interferomery (AMI)

## Slide 13: Probing JWST’s highest angular resolution
Simulation of 1-2 Mjup planet at 1 AU of an M0V located at 10 pc. Observing time: 3 hrs

## Slide 14: Wide field slitless spectroscopy (WFSS)
NIRISS can do wide-field slitless spectroscopy in FOV 2.2’ x 2.2’
Two orthogonal R=150 grisms and six blocking filters from 0.9 to 2.2 microns

## Slide 15: Wide field slitless spectroscopy (WFSS)
What is NIRISS Wide-Field Slitless Spectroscopy capable of?
Spectra of all objects in the field
In a ‘’blank’’ field there are ~3000 galaxies at mag < 28  high multiplex factor
Almost complete spectral coverage from 0.9 to 2.2 microns
At least one strong emission line from z=0.5 to z=4.9. Ly alpha if present at 6<z<17
Resolving power 100 to 200. Most spectral lines are unresolved, so a map of emission line is possible with WFSS.
Spatial resolution: 0.06’’ ~0.5 kpc
Cross-dispersed grisms to mitigate contamination
Point-and-shoot observing – no target acquisition
Ideal for pure parallels due to simple operation
CV3 data

## Slide 16
Brammer et al. 2012.
Surveys with WFC3-IR on HST have highlighted
capabilities of space-based near-IR grisms

## Slide 17: Wide field slitless spectroscopy
Model emission line sensitivity with various band-limiting filters

## Slide 18: WFSS continuum sensitivity

## Slide 19: WFSS simulations of Frontier Field MACS0416
F200W + GR150R
F200W + clear

## Slide 20: WFSS simulations of Frontier Field MACS0416
F200W + GR150R
F200W + clear
Zoom-in to 1% of the field shows many faint galaxies with emission lines

## Slide 21: WFSS simulations of GN-z11
Oesch et al. 2016
Below is a NIRISS simulation of Oesch et al. (2016) z=11 galaxy
Exposure time: ~3 hours per filter
NIRISS WFSS will get continuum break redshifts even if no Lyman-α

## Slide 22: Outline
Introduction – historical background
Instrument overview
Observing modes
NIRISS GTO program overview

## Slide 23: NIRISS GTO in brief
NIRISS team has 450 hrs (wall clock time)
Two core programs
  High-z galaxies with WFSS (~200 hrs)
  Exoplanet characterization (~200hrs)
    Transit, eclipse and phase curve spectroscopy with SOSS
    High-contrast imaging with AMI
Miscellaneous programs (~50 hours)
  AGN imaging with AMI
  Sub-stellar IMF in young clusters with WFSS
  …

## Slide 24: The Canadian NIRISS Unbiased Cluster Survey
NIRISS High-z Working Group
Bob Abraham
Loic Albert
Gabe Brammer
Pierre Chayer
Van Dixon
Rene Doyon
Jean Dupuis
Laura Ferrarese
Paul Goodfrooij
John Hutchings
Andre Martel
Swara Ravindranath
Marcin Sawicki
Chris Willott
Studying the Universe in and behind massive lensing clusters

## Slide 25: Science Goals
Primary
The Evolution of Dwarf Galaxies
Galaxies in the Reionization Epoch
Massive Clusters and Cosmography
Secondary
Quenching
Merger Rate
Environments
Transients
The proposed survey emphasizes two unique features of Wide Field Slitless Spectroscopy with NIRISS:
Very high multiplex factor
Spatially-resolved emission lines

## Slide 26: Survey Design

## Slide 27: Survey Design
We will observe six strong-lensing galaxy cluster fields at 0.35<z<0.7. Large sample of distant galaxies (~3000 at z>1.7).
The NIRISS integration time of 6.3 hours per filter will produce unrivalled deep slitless spectroscopy more than an order of magnitude deeper than previous studies with Hubble at much higher spatial resolution and wider wavelength range.
Target list to be finalized April 2017.

## Slide 28: Summary
NIRISS has unique and complementary/redundant capabilties with NIRCam (imaging) and NIRSpec (MOS).
NIRISS Wide-Field Slitless Spectroscopy provides a powerful alternative/complement to NIRSpec MOS when high redshift completeness required.
Low resolution grism spectroscopy particularly important for emission line maps of low-luminosity galaxies